## Slide 1: Introduction to Motion Control
Rochester MakerSpace
2021

## Slide 2: Class Objectives
Become familiar common types of motors
Focus on motors typically used by hobbyists
Understand how to control motors
Understand cautions when using motors with microcontrollers/microcomputers
Provide projects to demonstrate motor control on Raspberry Pi and Arduino
Provide examples of typical motor applications
Provide list of resources for learning more

## Slide 3: Class notes and code
All the class notes and code can be downloaded from GitHub:
  https://github.com/RochesterMakerSpace/MotionControlClass
Pull down the green “Code” button and select “Download ZIP”

## Slide 4: Types of Common Electric Motors
There are two main motor classifications, ac and dc, with three application areas, constant speed, variable speed and position (or torque) control.
AC Motors
  AC motors are typically associated with industrial applications and will not be address further in this class.
DC Motors
  Although large DC motor are common in industrial application smaller DC motor are favored by the hobbyist and include:
  DC Brushed Motors – simple, cost effective, lightweight and easy to control. Excellent torque at low speed but produce electrical noise. Used as drives for hobby vehicles.
  DC Brushless Motors -- mechanically simpler than brushed motors but require more complex controllers and gearboxes and can be found in multicoptors and drones.
  Servo Motors – good for projects needing precise control of angular or linear position such as robots.
  Stepper Motors – move in discrete, precise steps and are found in CNC machines and 3D printers.

## Slide 5: Brushed DC Motor Description
  Components:
    Stator: Generates a stationary magnetic field that surrounds the rotor
    Rotor (armature): Made up of one or more windings. Produce a magnetic field when energized
    Brushes: As the motor turns, carbon brushes slide over the commutator, coming in contact with different segments of the commutator
    Commutator: Segments are attached to different rotor windings, generating a dynamic magnetic field inside the motor.

## Slide 6: Brushed DC Motor Example
DC Gearbox Motor – “TT Motor” – 200 RPM – 3 to 6 VDC
  Operating Voltage Range: 3~7.5V
  Rated Voltage: 6V
  Max No-load Current (3V): 140 mA
  Max No-load Current (6V): 170 mA
  No-load Speed (3V): 90 rpm
  No-load Speed (6V): 160 rpm
  Max Output Torque: 0.8 kgf cm
  Max Stall Current: 2.8 A
Pololu Micro Metal Gearmotor
  See spec sheet

## Slide 7: Brushed DC Direction Control: H-Bridge
An H-Bridge circuit contains four switches with the motor at the center forming an H-like arrangement.
Closing two particular switches at the same time reverses the polarity of the voltage applied to the motor. This causes change in spinning direction of the motor.
The control circuit prevents closing both switches on the same side of the H-Bridge, thus preventing a short from Vcc to GND.

## Slide 8: Brushed DC Speed Control: PWM

## Slide 9: Brushed DC Motor Drivers
Model | L298N | TB6612 | DRV8833 | DRV8871
Current | 2A | 1.2A | 1.5A | 2A
Peak Current | 3A | 3.3A | 2A | 3.6A
Operating Voltage | 3.2 – 40 V | 4.5 – 15 V | 2.7 – 10.8 V | 6.5 – 45 V
Efficiency | 40-70% | 91-95% | 70-90% | 
Total MCU pins | 6 | 6 | 4 | 2
PWM Pins | 2 | 2 | 2/4 | 2
Number of motor outputs | 2 | 2 | 2 | 1
Technology | Bipolar | MOSFET | MOSFET | MOSFET
Approximate cost | $2.50 | $5.00 | $5.00 | $7.50

## Slide 10: Servo Motor Description
Components:
  Motor
  Potentiometer: Shaft position
  Gear Assembly: Reduce RPM to increase torque
  Controlling circuit: Feedback
  Input signal: PWM pulse width
An error signal is generated between the potentiometer and the input signal. The error signal causes the motor shaft to turn, changing the voltage on the potentiometer, thus reducing the error until the motor stops when the error is 0.

## Slide 11: Brushless DC Motor (BLDC) Description
Brushless DC motor control is not quite as simple as the regular brushed type. Brushless motors require a controller that can sense the proper time to reverse the voltage to the coils.
Some motors have built-in hall-effect sensors that can detect the orientation of the rotor. Controllers for this type of motor require sensor inputs to read these hall sensors.
Other 'sensorless' motor controllers sense the back EMF in the motor coils themselves to detect the rotor position. Most ESC (Electronic Speed Controls) for brushless RC motors use this technique.
Brushless motors designed for autonomous and remote control aircraft and vehicles typically require a separate controller. These are typically of the sensorless type and use standard servo type pulsed signals for speed control.
Applications include RC controlled planes and drones.

## Slide 12: Brushless DC Motor (BLDC) Description

## Slide 13: Servo/BLDC Control

## Slide 14: Stepper Motor Description
Advantages
  Steppers don’t require a sensor to detect the motor position since the motor moves by simply counting steps.
  Although the motor does need a controller it doesn’t need complex calculation or tuning to work properly.
  With micro stepping high positional accuracy can be achieved.
  Good torque at low speed and great for holding position.
Disadvantages
  Can miss steps if torque load is too high.
  Always drain maximum current.
  Low torque and noisy at high speeds.

## Slide 15: Bipolar Stepper Motor Example
TPP-47-002
  NEMA 17
  Step Angle: 1.8 degree (200 steps/rev)
  Holding Torque: 33Ncm(47oz.in)
  Rated Current/phase: 1.2 A
  Phase Resistance: 2.4 ohms
  Inductance: 4.7 mH
  Application: 3D Printer

## Slide 16: Bipolar Full Step Sequence

## Slide 17: Unipolar Stepper Motor Example
28BYJ-48
  Rated Voltage: 5V DC
  Number of Phases: 4
  Stride Angle: 5.625°/64
  Pull in torque: 300 gf.cm
  Insulated Power: 600VAC/1mA/1s
  Coil: Unipolar 5 lead coil

## Slide 18: Unipolar Full Step Sequence

## Slide 19: Stepper Motor Half Step Sequence

## Slide 20: Stepper Motor Drivers
Model | DRV8825 | A4988 | TMC2208 | ULN2003
Type | Bipolar | Bipolar | Bipolar | Unipolar
Max Current per coil | 2.2 A | 2.0 A | 2.0 A | 600 mA
Continuous current per coil | 1.5 A | 1.0 A | 1.2 A | 
Max step resolution | 1/32 | 1/16 | 1/256 | N/A
Logic range | 2.5 – 5.25 V | 3 – 5.5 V | 3 – 5 V | 5 V
Supply Voltage Range | 8.2 – 45 V | 8 – 35 V | 5.5 – 36 V | 50 V
Interface | Step/Dir | Step/Dir | Step/Dir | Channels
Approximate cost | $9.00 | $2.00 | $15.00 | $1.50

## Slide 21: Integrated Stepper Motor Driver
gShield v5
  ~ $50
  Arduino Uno Shield
  3x TI DRV8818 Stepper Drivers
  Runs grbl firmware
  https://github.com/gnea/grbl
  Application: CNC Router

## Slide 22: Integrated Stepper Motor Driver
RAMPS 1.4
  ~ $20 including DRV8825 Motor Drivers
  Arduino Mega Shield
  Different drivers may be used
  Runs Marlin firmware
  https://marlinfw.org/
  Application: 3D printer

## Slide 23: Project – Brushed DC Motor
Driver: L298N
Raspberry Pi Wiring
  IN1 to GPIO26
  IN2 to GPIO19
  IN3 to GPIO20
  IN4 to GPIO16
Set power supply output to 7.4 V
Open MotionControlClass/BrushedDC/key_brushedDc.py using the Geany IDE
Run key_brushedDc.py
Put cursor focus in terminal window that pops up.
Arrow keys to move motors.
Enter key to stop
‘q’ to terminate program

## Slide 24: Project – Servo Motor
Use mechanical crane
Raspberry Pi Wiring:
  Servo Pan: GPIO18
  Servo Tilt: GPIO17
Set power supply output to 5V
Open MotionControlClass/ServoMotor/key_ServoMotor.py using the Geany IDE
Run key_ServoMotor.py
Put cursor focus in terminal window that pops up.
Arrow keys to move motors.
Enter key to stop
‘q’ to terminate program

## Slide 25: Project – Brushless DC Motor
Driver: ESC
Guide: https://howtomechatronics.com/tutorials/arduino/arduino-brushless-motor-control-tutorial-esc-bldc/
Arduino Wiring:
  Speed control: Pin 9 (White)
  Pot Wiper: A0 (Green)
Set power supply output to 12V but do not enable the power supply
Open MotionControlClass/BldcMotor/BldcMotor.ino using the Arduino IDE
Upload the sketch
Turn pot full clockwise
Enable the power supply
The motor speed is controlled with the pot. If the pot is full on (counter clockwise) on then the motor will not start and must be calibrated (see Guide).

## Slide 26: Project – Unipolar Stepper Motor
Driver: ULN2003
Guide: https://www.makerguides.com/28byj-48-stepper-motor-arduino-tutorial/
Arduino Wiring
  IN1 to Pin 11
  IN2 to Pin 10
  IN3 to Pin 9
  IN4 to Pin 8
Set power supply output to 5V
Open MotionControlClass/UnipolarStepper/BasicUnipolarStepper/BasicUnipolarStepper.ino using the Arduino IDE
Upload the sketch
The motor will rotate 1 revolution, reverse and rotate 1 revolution in the opposite direction and repeat forever.

## Slide 27: Project: Unipolar with ATTiny
Driver: ULN2003
Plug in 28BYJ-48 motor with red wire nearest C3/C4
Power board with USB-C power block
The motor will rotate in the clockwise direction looking at the shaft side of the motor.

## Slide 28: Project: Unipolar with ATTiny
static inline void decrMotor( void ){
switch( MotorState ){ //prior to decrement
case 7: //1001->X___->0001
clear_bit( S1_PORT, S1 );
break;
case 6: //0001->__^_->0011
set_bit( S3_PORT, S3 );
break;
case 5: //0011->___X->0010
clear_bit( S4_PORT, S4 );
break;
case 4: //0010->_^__->0110
set_bit( S2_PORT, S2 );
break;
case 3: //0110->__X_->0100
clear_bit( S3_PORT, S3 );
break;
case 2: //0100->^___->1100
set_bit( S1_PORT, S1 );
break;
case 1: //1100->_X__->1000
clear_bit( S2_PORT, S2 );
break;
case 0: //1000->___^->1001
set_bit( S4_PORT, S4 );
MotorState = 8;
break;
} MotorState--;
}
This ATTiny code snippet demonstrates how to half-step sequence the ULN2003 driver. This function is called in a forever loop that includes a delay:
// ------ Event loop ------ //
while (1) {
  _delay_us( StepDelay_us ); decrMotor();
}

## Slide 29: Project – Bipolar Stepper Motor
Driver: DRV8825
Guide: https://www.makerguides.com/drv8825-stepper-motor-driver-arduino-tutorial/
Arduino Wiring:
  EN (Enable impulse): jumper to GND
  DIIR: Arduino Pin 3
  STEP: Arduino Pin 2
  5V INPUT: Arduino 5V and GND
Set power supply output to 12V but do not enable the power supply
Adjust current limit according to Guide: Current Limit = Vref X 2 (will have to enable power supply)
Open MotionControlClass/BipolarStepper/BasicBipolarStepper/BasicBipolarStepper.ino using the Arduino IDE
Upload the sketch
Enable the power supply output
The motor will slowly in both directions for one revolution and then faster in both directions for several revolutions
Try changing subdivision control: Disable power supply, change DIP switch, Enable power supply